1. TestOne
  1. A simple transition from zero to one includes how many frequencies?
    1. - An infinite number
  2. I2C is what kind of communication?
    1. - Synchronous
  3. A protocol transmits 1 byte at a time through a serial connection at 9600 bits
    per second with 1 start, 1 stop, and no parity bit. What is the minimum time it
    will take to transmit 72000 bytes or octets?
    1. - 75s - remember you are doing 9600 BITS not bytes so it is going to be really slow.
  4. What is the lowest layer of the OSI 7-layer network diagram?
    1. - Physical
  5. RS232 or 'Serial' port use a common ground and...
    1. - a transmit and a recieve wire.
  6. what is the odd-parity of 0110?
    1. - 1
  7. Bits or bytes of information to verify that both sides of a communication have the same data at the end of the reception are named?
    1. - CRC or Checksum
  8. Bits or Bytes of data to synchronize the timing on both sides of a communication channel are usually named?
    1. - Framing
  9. What is the second lowest layer of the OSI 7-layer Network?
    1. - Data Link
  10. SPI uses a common ground and
    1. - A master in slave out, a master out slave in, a clock and a slave select.
  11. RS-232 (Serial Ports) are
    1. - Still used even virtualized today
  12. CRC stands for
    1. - cyclic redundancy check
  13. If data is being transmitted at 9600 baud what is probably true about the wiring and hardware on both sides of the communication?
    1. The wire and hardware can be poor quality.
  14. A transmission approach that does not have a separate clock line is said to be?
    1. - asynchronous
  15. FM communication
    1. - Changes frequency of the transmitted signal
  16. SPI (Serial Peripheral interface) bus is an example of which type of communication?
    1. - Synchronous
  17. AM communication
    1. - Changes volume of the transmitted signal
  18. A simple on/off signal on a wire that a fixed frequency contains
    1. - infinite harmonics
  19. I2C uses a common ground
    1. - a data and a clock wire
  20. High speed data transmission
    1. - better quality wire/fiber optics and more precisely timed equipment
  21. A transmission approach that does have a separate clock line is said to be
    1. - synchronous
  22. Preamble bits or bytes are used to
    1. - synchronize timing and stabilize the AGC
  23. SMTP stands for
    1. A Simple Mail Transfer Protocol
  24. Bits or bytes of nothing after data at the end of transmission are named?
    1. Stop or Gap
  25. To convert bps to Bps a quick rule is to
    1. divide by 10 - you have to cover the start and stop bit which makes 10 total bits.
  26. BAUD rate and bps would be different if
    1. at any moment more than a single 1 or 0 is transmitted.
2. TestTwo
  1. How many servers on a single computer can use a socket on port 1025?
    1. 1 because it binds the socket
  2. DD-WRT is firmware from
    1. an open source community for consumer routers
  3. The C/C++ function ‘connect is the moment in code where the ____ makes a connection over the network.
    1. client
  4. DHCP performs what operations for networked devices?
    1. Hands out ip addresses to new machines that connect
  5. Which protocol has acknowledgments of Datagrams received?
    1. TCP
  6. The port number for PING is
    1. There is no port number
  7. When a user copies a file over a network it is usually
    1. chopped into pieces and sent in pieces
  8. If you want to send a file over the network and the protocol preserves order of packets, you are probably using
    1. TCP
  9. What is the third lowest layer of the OSI 7-layer network diagram?
    1. Network
  10. What is special about port numbers less than 1024
    1. Originally they were reserved for root/super user privileged servers.
  11. How many clients on a single computer can connect on a socket on port 1025
    1. infinite or limited to number of process in the operating system
  12. Most networks today are of a ___ configuration.
    1. Star
  13. HTTP stands for
    1. Hyper Text Transmission Protocol
  14. The C/C++ function ‘ bind’ is the moment in code where the _____ gets exclusive hold of the socket?
    1. Server
  15. If you want to send a packet of information over the network and your protocol does not care if it arrives you are probably using?
    1. UDP
  16. What is the second lowest layer of the OSI 7-layer network diagram?
    1. Data-Link
  17. What is the lowest layer of the OSI 7-Layer network diagram
    1. Physical
  18. DNS performs what operations for networked devices?
    1. Converts names like www.google.com to ip address
  19. SMTP stands for what?
    1. Simple Mail Transfer Protocol
  20. The port number for HTTP is?
    1. 80
  21. Email is _____ when sent over network
    1. not encrypted
  22. To convert bps to Bps a quick rule is to
    1. divide by 10
  23. NAT performs what operations for networked devices?
    1. Maps WAN ip addresses to LAN ip addresses
  24. Apache is a daemon (no UI executable)
    1. for serving web-pages